## Slide 1: Side Scan Data Processing
HYPACK 2020 Training Event
January 2020

## Slide 2: Overview

## Slide 3
Mosaic Data Flow
HYSWEEP SURVEY
SIDE SCAN
SURVEY
SIDE SCAN MOSAIC PROGRAM
(HYSCAN)
HSX
HSX
Side Scan Data
TIF
24 or 8 bit
TIF
TIF
TIF
Line 1
Line 2
Line 3
TGT
Mosaics
TIF
TIF
TIF
Targets
Average Backscatter Data from Multibeam
Entire Data Set
Individual tifs can be created from each line, or a single tif from all lines
Targets can be saved into a report and displayed in Target Viewer.
HSX files created in Data Converter
HS2 or XTF
3rd PARTY SIDE SCAN
FILES
CM2
JSF
SDF
XTF
Notes: 3

## Slide 4
Icons in Side Scan Mosaic
Load Files (HSX, HS2, XTF, JSF, SDF, CM2)
Save to HS2 File
Raw Data Mode – displays altitude, heading, and tracks
Scan View – displays waterfall and target captures
Mosaic View – dialog for creating mosaic
Redraw Screen
Sidescan Controls
Next/Previous Line Selection
Remove Line
Notes: 4

## Slide 5
Side Scan Mosaic Processes
Stage 1: Raw View
  Load raw side scan data – HSX, HS2, XTF, JSF, SDF, or CM2 files
  Adjust bottom track, smooth heading and track line data.
Notes: 5

## Slide 6
Side Scan Mosaic Processes
Stage 2: Scan View
  Full line can be scrolled through
  Adjust color, gain, TVG, and display options (water column removal, display range of sonar image)
  Capture and measure targets (GeoTIFF and JPG images)
Notes: 6

## Slide 7
Side Scan Mosaic Processes
Stage 3: Mosaic
  Create mosaics, export GeoTIFF images
  Apply image filters
  Ability to use a Border file for mosaic creation in specific area
Notes: 7

## Slide 8: Loading and Stage 1

## Slide 9: Loading a File, pt. 1
Select “Open File” from the main window
Navigate to either the Raw or the Edit folder
Select the lines you are interested in
Adjust the Read Parameters

## Slide 10: Loading a File, pt. 2 (Read Parameters)
Selections: Choose a sonar, navigation, and heading device
Device Info: Set offsets
Survey Info: Basic data from the survey
Advanced:
  Apply smoothing to the bottom track, heading, and navigation
  Adjust the bottom track up or down
  Advanced XTF options
  Apply median filter to the data
  If device numbers change between files, attempt to match them
Notes: Attempt to match devices between files: For example, if, in file 1, the first device is navigation and the second is the sonar, and in file 2 the first device is sonar and the second navigation, it will detect that and swap them

## Slide 11
Stage 1: View and Options
Heading Window: Smooth heading
Navigation Window: Smooth position
Towfish Altitude Window:
Review and edit bottom detection
Smooth and lower bottom detection
Note: | Adjustments to the file will be used in mosaicking process. Saving these adjustments to an HS2 file will allow you to re-load the files with adjustments already done

## Slide 12
Stage 1: Altitude and Heading data
Adjusting Heading and Trackline
Option to remove navigation spikes and smooth data
Heading can be smoothed between two points, or the entire line
Original data is drawn as background for comparison to smoothed data
In View - Options:
Display the data without the swath
Select the smoothing filter
Notes: | The smooth option can be done multiple times. On a fixed mount system, smoothing may not be needed. There is a counter to track the number of times smoothed
Notes: Positions can be selected or excluded for smoothing
Areas can also be selected to exclude from the final imagery
Right-click -> Show Charts
12

## Slide 13
Stage 1: Bottom Tracking
Towfish altitude view. The blue line should closely follow the bottom
Choose port or starboard
If you already have a decent bottom track, skip to step 4
If there is no bottom tracking, use the Auto Bottom Detection feature
    Set a blanking
    Set a gate size
    Set sensitivity
    Click Apply
Use the Digitize button to manually set the bottom
Use the Smooth button to smooth the altitude
Use the Up/Down arrows to move the altitude up or down slightly
Notes: | Gains are not applied in stage 1
Notes: 13
Blanking: How much of the swath to ignore. Move your mouse to the highest point where imagery appears and copy the Range (near the top) into the Blanking field.
Gate Size determines how much above or below the last ping’s altitude to look for the current ping’s altitude. If no altitude is found in the gate, it will ignore the gate and find a new altitude.
Sensitivity: Higher sensitivity will use samples with lower returns for the bottom, while lower sensitivity will use samples with a higher return for the bottom. Generally, high sensitivity will return a higher altitude than low sensitivity.
Digitize: Click to enter “digitize mode”. Click on the imagery to set the altitude. When finished, click the digitize button to exit digitize mode and set the altitude.

## Slide 14: Stage 2 and Adjusting the Image

## Slide 15
Stage 2: Features & Options
Adjust side scan image
Create and measure targets
Export data to spreadsheet
Save non-georeferenced image
Adjust layback
Save coverage map as GeoTIFF file
Notes: 15

## Slide 16: Bottom Tracking in Stage 2
To bottom track in stage 2 the user selects the Digitizing tool and then selects the first bottom return.
Reselect the digitizing tool applies the new bottom track

## Slide 17: Sidescan Controls - Colors
Right-Click -> Sidescan Controls, View->Sidescan Controls, or Shift + F9
“Edit Custom Palettes” opens a window where you can create your own color palettes
“Waterfall Downsampling Method” (PDF) is used when choosing what color a pixel uses to represent a set of samples

## Slide 18
Color Palette Choices
GRAY
GOLD
RUST
COPPER
PASTEL
INTENSITY
Notes: 18

## Slide 19: Sidescan Controls - Gain
Basic Gains: Adds dB over time
    NOT “base gain”
    Channels can be adjusted separately
Auto TVG: “Smart” TVG
    Higher sensitivity creates a brighter image
    Across-Track-Smoothing creates a smoother curve
dBs / 100 Meters: Multiplies dB over time
Formula: Applies the shown formula, where ‘r’ is range
Angle-Varied Gain looks forward & backward by a number of pings (or full line option) at a constant grazing angle to normalize the backscatter.

## Slide 20: Sidescan Controls - Display
Show range marker for other frequency: In multi-frequency datasets, draw an indicator in Stage 2 Scanview marking the range of the other frequency
Clip range to NOAA guidelines: If the altitude is less than 8% of the range, set the range to altitude X 12.5.

## Slide 21
Saving Image as BMP file
Use the Save tool to save an image of the entire waterfall. This is a non-georeferenced file, but holds all details of the imagery.
Notes: 21

## Slide 22
Spreadsheet Options
Set-up dialog box
Note: Use Tools->Adjust Layback to modify layback for entire file
View->Spreadsheet if not visible
View->Options (or F9), Spreadsheet tab
  Configure spreadsheet for desired fields
Output data to a single file or multiple files
Use to adjust Layback for individual pings
Notes: 22

## Slide 23
Saving Coverage as TIF file
Current view in display is bounded by blue box
Display coverage of all tracks, background charts & soundings
Current view in display is bounded by blue box
Red represents port side, green represents starboard side
Save image as GeoTIFF file (right click on image or click the camera button)
Notes: 23

## Slide 24
Using Coverage Map to Manage Targets
Blue bounding box = previous line
Red bounding box = current line.
Note the difference in position (approx. 2 meters) when viewed in Scan View. Possible cause could be slant range correction differenced due to bottom tracking.
When a target is taken, a mark is generated on the coverage map. Use this feature to verify location or to confirm target.

## Slide 25: Targeting

## Slide 26
Targeting
Select Target (double left-click on feature)
Target window opens
In Stage 2, double click on any feature.
Use sliders to determine the 3 points along the target. Use the signal display to help.
Click and drag to measure contact, capture JPG or TIF and enter any notes
Targets are saved to the Target Database for viewing in other HYPACK programs
Notes: 26

## Slide 27
Bulls-eye icon:
Select, then in Scanview, click an object of interest.
A target will be created with an image.
(Shift-right click will remove a target)
Options available to adjust targeting
In HYPACK, check “Side Scan Images” folder to view targets
Targeting – Marking Targets Quickly

## Slide 28
Target Viewer
Use the target viewer to examine all targets
Arrow keys to scroll through the list of targets
Data fields are editable
Report can be saved to a RTF file
TargetViewer.exe program can run without a HYPACK key
Notes: 28

## Slide 29
Target Classification Database
Launch from HYPACK->Side Scan-> Target Classifications
Create/Edit/Delete a classification
Add/Delete a reference image
Scroll through existing images
How “confident” you are an image belongs to this classification (0-7)
Notes: 29

## Slide 30
Target Classification Database
In Target Viewer, select from classification drop down the targetID
Use the ? To open the comparison window
Target classification comparison
Target Viewer

## Slide 31: Stage 3: Mosaicking

## Slide 32
Stage 3: Side Scan Mosaic
Notes: 32

## Slide 33
Stage 3: Mosaic
Select files to mosaic
Enter resolution
Select Overlap & Filter methods
Single TIFF or one per line
Use Border file for specific area mosaic
Name the TIFF file
Display can show Track Swath Coverage, Targets (from Phase 2) and Border file outline. Use Options (F9) or right click on the display to enable coverage lines.
Notes: 33

## Slide 34: Blanking the Nadir region for Mosaic
The user can control the Nadir region by applying a distance from Nadir to ignore returns. Using this feature will remove the heavy shaded area along the boat track.
Use this feature if you have overlap in the Nadir Region

## Slide 35: Resolution Calculator
Determine the optimal mosaic resolution based on your sonar's characteristics
Don't waste time and space on heavily-interpolated imagery
Calculate along-track and across-track resolution
Load & Save sonar profiles across HYPACK projects
When closed, the best resolution is applied to the mosaic setup

## Slide 36
Mosaic Filter Options
AVERAGE:
Smooths the mosaic by setting each pixel to the average of the 3x3 pixel neighboring cells.
SHARPEN:
Sharpens the mosaic by enhancing pixel contrast relative to a 3x3 pixel neighboring cells.
MEDIAN:
Smooths the mosaic while preserving edges by setting each pixel to the 3x3 median value.
Notes: 36

## Slide 37
Tiling of Mosaics
Based on the resolution and the extents of your mosaic, HYSCAN may decide to sub-divide your mosaic into several GeoTIFF files.
This allows you to mosaic a big area at a high resolution.
It takes a little longer, but you’ll get the detail you need.

## Slide 38: Saving, Batch Mosaicking, and Merge Mosaics

## Slide 39: Saving Your Data:
Data can be saved as:
  HS2 – All settings (gain, bottom track, navigation editing) are saved.
  XYIntensity – Each point will have an intensity value.
  Export to XTF – Creation of XTF files for non-HYPACK programs.

## Slide 40
Batch Mosaicking
Run SIDE SCAN MOSAIC (HYSCAN) all the way to Stage 3.
Enter all settings and then select “Add to Batch File…”.
Close SIDE SCAN MOSAIC program without generating the mosaic.
When you are ready to make a mosaic, run SIDE SCAN AUTO MOSAIC
Running SIDE SCAN AUTO MOSAIC
Notes: 40

## Slide 41
Merge Mosaics
Run SIDE SCAN MOSAIC (HYSCAN).
Generate a separate mosaic TIF for each file.
Run SIDE SCAN MERGE MOSAICS to combine the separate TIFS into a single TIF.
TIFF
TIFF
TIFF
TIFF
TIFF
Line 1
Line 2
Line 3
Line 4
Line …..
SIDE
SCAN MOSAIC
SIDE
SCAN MERGE MOSAICS
TIFF
Separate TIFF File for Each Survey Line
Single TIFF File Composed of All Individual TIFF Info
Notes: 41

## Slide 42: Thank You !
January 2020
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500